## Slide 1: STM32 WRITING ROBOT
GROUP 57
Chiu Chi Keung
Yu Yingxuan

## Slide 2
Functionality
PC words input
  Words input from PC UI
Draw shapes
Arbitrary direction and length, at assigned location
  Data conversion to STM32
  Writing with vector data

## Slide 3
Core Principle: BasicMove & CoreXY
BasicMove
  Simple, ease to use & call
  Octo-directional
  Time-based
  Good for:
  Simple drafting
  logos
(legacyMove)

## Slide 4
Core Principle: CoreXY
Two Motion Motor
  Moves in diagonal
    When one motor spins, “L” shaped belt changes length
  Why?
    CoreXY VS Cartesian: more light weight, faster
    Each motor have control to both X and Y axis
    Use both motor for single axis movement
One Pen Lift Motor
  Control Pen up and down

## Slide 5
void motorControl(delta_MotorL, delta_MotorR)
  Support Draw and Writing of any vector
  delta_Motor(L/R):
    Motor Spin how much & in what direction
  Bresenham's line algorithm:
    move in X and Y alternately, in fixed step size (like zigzag)
    WorkFlow :
    Find absolute steps of each Motor: the larger is base
    Setup appropriate error
    First, move from the base axis, error adds up
    Then, error in that axis exceeded, change axis
    Alternate until the vector is drawn
    PWM supported: adjust writing speed / step size
CoreXY: Mechanics

## Slide 6
void updateGlobalXY(delta_X, delta_Y)
  Update position data
void moveToAbsoluteXY(target_X, target_Y)
  Move to designated position
  Calls moveToXY()
CoreXY: Drawing/Writing functions
void moveToXY(delta_X, delta_Y)
  Basic writing command
  Calls motorControl() and updateGlobalXY()
void moveAngle(distance, angle)
  Translate the math units into steps for Motor
  Calls moveToXY()

## Slide 7
CoreXY: Drawing
Pentagon
Circle

## Slide 8
Writing: How it works
Transmission:
USB Change Data Capture (CDC) Client:
capture the JSON data and validate, then pass data to Parsers
STM32:
Parsing: parse incoming JSON data into C data structures, then feed to writing instructions
PC User Interface:
Input: word input in interface textbox, page data in the data box
Convert: JSON data

## Slide 9
Writing: PC User Interface

## Slide 10
Writing: USB Change Data Capture
(CDC) Client
USB CDC Interface:
Transmits data:
Data Flow Protocol:
Handshaking mechanism:
Buffer Management:
for character data: charBuffer
document information first,
for document: infoBuffer
CDC_Receive_FS() callback function
CDC_Transmit_FS() function
with Ready and End signals
virtual serial port over USB
Handles data :
Two-phase transfer:
Separate buffers:
then character by character data

## Slide 11
Writing: Data structure (in STM32)
Data hierarchy
  Document: Data of the page, Segment within (page width…)
  Segment: Group of characters, inter-line data (line gap…)
  Character: combination of Vectors, inter-character data (line feed…)
  Stroke: Vector data between points
  Points: Position data (x & y)
  Document -> Segment-> Character -> Stroke -> Point
  Unfortunately: Due to limited memory in STM32 (64kb), structure must be changed during transmission

## Slide 12
Writing: Data structure (during transmission)
Data hierarchy
  Document: Data of the page, Segment within (page width…)
  Segment: Group of characters, inter-line data (line gap…)
  ----------------------------------------------------------------------------------------------
  Character: combination of Vectors, inter-character data (line feed…)
  Stroke: Vector data between points
  Points: Position data (x & y)
  Document -> Segment
  Character -> Stroke -> Point
Character-by-Character Transmission

## Slide 13
Writing: Two Essential instructions
"114514"
  The STM32 sends it to the PC to indicate that it is ready for the data for the next character
"1919810"
  The PC sends it to the STM32 to indicate that the data just sent is the last character data of the task, and the STM32 should expect new global information of the next writing task

## Slide 14
Writing: The Working Loop
The working loop:
  Setup (if a new job found)
    Processes and Parses document information received via USB
    Initializes structures, dimensions and environment
    Enables motors
    Sends "114514" to PC
  Writing
    Processes and Parses character information received via USB
    Writes individual words (vector) and manage environment (line feeds, change position, etc)
    Sends "114514" to PC after the writing job one character has finished
  Cleanup (if a job is completed)
    Frees all allocated memory
    Resets all global variables
    Disables motors

## Slide 15
Writing: Data Flow
Data initialization & processing:
  process[data]() to process incoming data from USB
  parse[type]() to convert received data into [type]
  init[type]() to create empty container
  E.g.:
  processChar(*buffer, length) : Catch incoming JSON data, then call initCharacter(), and pass the JSON to parseCharacter().
  parseCharacter(*character, *json) : Parse JSON data into a Character properties and related structure.
  initCharacter(*character, …) : Create empty Character(s).

## Slide 16
Writing: Data handling
Process:
  Processes data received over USB (Change Data Capture Client)
  Creates global ‘current’ structures (to point at the data working at)
  Sets up initial position and sends ready signal
Parse:
  Extracts page dimensions and environment data
  Parses JSON data into C structures that STM32 can read
Initialize
  Initializes C Structures with given data
  Allocates dynamic memory for Structures

## Slide 17
Writing: The Act
With appropriate C structures and data:
  Draw:
    Use relative or absolute position data to position the structure
    E.g.:
      Segments positioning with line_gap
      Character relative placement
      Stroke's location and vector
    Calls Writing functions (e.g. moveToAbsoluteXY) : all data is processed to groups of vectors

## Slide 18
Development: Issues We Faced
Wi-Fi module out of grasp:
  The system is too complicated
  Resolution:
  Use USB CDC instead
CDC can only transfer 64 bytes at once:
  Resolution:
  Sectioned transmission
    .json data is spliced into sections of 32 bytes
    Each is transmitted with 10ms of delay accordingly

## Slide 19
Development: Issues We Faced
STM32 Limited Memory:
  During development – not aware of very limited Memory
  Document exceeded limit
    structure Writing the ‘whole’ document is not possible
  Memory cannot hold a full JSON data file
    Sending the whole file is not possible
  Chinese words’ data cannot be fully sent (plan discarded)
  Resolution:
  Break down data from PC
    Two-phase transfer: Document mostly store environment data, Character mostly store word data
    Discrete word data: Character mostly transfer one after one, then freed immediately

## Slide 20: Thank you

## Slide 21: References:
https://blog.csdn.net/weixin_43492610/article/details/122628863
https://blog.csdn.net/xusiwei1236/article/details/141504722
https://blog.csdn.net/qq_25626001/article/details/119354210
https://shequ.stmicroelectronics.cn/thread-637593-1-1.html
https://www.geeksforgeeks.org/bresenhams-line-generation-algorithm/
https://www.geeksforgeeks.org/change-data-capture-cdc/